## Slide 1: SHARPS INJURY PREVENTION IN THE INTRAOPERATIVE SETTING

## Slide 2: .
Presented by: Pascalia Ojakaa
BScN/ORN

## Slide 3: Objective
To provide knowledge of best practices related to sharps safety:
Hands-free technique in reducing the incidence of percutaneous injuries, contaminations, and glove tears arising from handling sharp instruments.

## Slide 4: What is sharp injury
A sharp injury is a penetrating stab wound from a needle, scalpel, or other sharp object that may result in exposure to blood or other body fluids.(CDC)

## Slide 5: Background
It is estimated nearly 600,000 to 800,000 percutaneous injuries that occur annually among healthcare workers.
Research indicates injuries from sharp devices occur in 7-15% of all surgical procedures.
Surgeons and First Assistants/Residents have the highest risk of injury at 59%.
Scrub personnel have the second highest frequency at 19%.
Anesthesia personnel and circulating nurses are the third highest at 6%.

## Slide 6: Impact of sharp injuries
Psychological toucher/Anger
Absenteeism
Presenteeism
Infections

## Slide 7: Factors Influencing Exposure
Type of surgical procedure
Characteristics of the device & equipment used
Nature of work
Space and visibility within operative fields
Level of staffing
Frequency of emergency patient care situations
Pace of work

## Slide 8: Most Injuries Occur when:
i) Loading Needle Holder
ii) Hand to Hand passing of needles between scrub nurse and surgeon
iii) Knot tying when a needle is attached to a suture
iv) When surgeon sutures/cutting toward themselves or to an assistant

## Slide 9: Most Injuries Occur Cont’
v) When retracting or stretching tissues with hands
vi) When placing used needle in an overfilled sharps container
vii) Loading or removing a disposable scalpel blade on a reusable knife handle
viii) Recouping of needles after use

## Slide 10: Risk Reduction Strategies
Practice “Hands Free” technique by Identify a “Neutral Zone”. This is designated area on the surgical field where sharps can be given to or received from the surgeon
Training of staffs on sharps safety
Monitor gloves periodically for punctures.
Use needle holder when unloading blades

## Slide 11: Neutral Zone

## Slide 12: scalpel disarmer

## Slide 13: Risk Reduction Strategies Cont’
Use needle holder when tying sutures knots
When cleaning instrumentation don non-penetrating gloves along with PPE’s to protect against accidental injury from sharp items
Use tongs to grasp instrumentation rather than reaching blindly into sink.

## Slide 14: Handling Instrument during Cleaning

## Slide 15: Other Strategies to Reduce Sharp Injuries
i) Keep track of and account for all sharp items.
ii) Keep hands away from surgical site when sharp devices are in use.
iii) When counting sharps in the needle book, always use an instrument to help separate for visualization.

## Slide 16: Other Strategies in Reduce Sharp Injuries
iv) Communicate location and use of neutral zone to the surgical team.
v) Give verbal notification when passing a sharp device.
vi) Organize work area so that sharps are pointed away from team members.
vii) The staff who generate the sharps is best placed to dispose them .

## Slide 17: Summary
Create a sharps safety educational training which focuses on improving handling of sharp, instruments and to enhance the surgical skills
Effective communication during surgery
Use the blade disarmer when unloading knife blades.

## Slide 18: Summary
Use of neutral zone that eliminates the hand to hand passing of sharps.
Use puncture resistant gloves and tongs when cleaning instrumentation

## Slide 19: Thank you